## Slide 1: Lead and Hazard Assessment

## Slide 2: History of Lead Use
https://www.youtube.com/watch?v=CM1u29BeqC0
Follow along with your worksheet
Notes: Worksheet can be found in the dropbox, titled “Lead Video Worksheet”

## Slide 3: What is Lead?
Soft-blue gray metal
Naturally occurs in the earth’s crust
Can be found in trace amounts in soil, plants, and water.
Still used in consumer products

## Slide 4: Common forms of Lead found in the Environment
Inorganic
  Form found in earth, paint, soil, and water
Organic
  Example- Tetraethyl lead in gasoline
  Form commonly found in work settings
  Can be more toxic because the body readily absorbs it

## Slide 5: Where can lead be found?
Notes: Have students break into groups of 3 or 4. Hand out cut outs of pictures of objects that may contain lead and objects that definitely don’t contain lead. Have students separate pictures into objects that contain lead and those that don’t. Give students around 5 minutes to complete. Have one representative from each group explain their choices, and explain them to students.

## Slide 6: How are you exposed to lead?
Notes: Looking at graphic, identify ways you are potentially exposed to lead. List on the worksheet.

## Slide 7: What properties of lead make it useful?
Soft and pliable
  Romans used it for their plumbing. Latin word for lead= “Plumbus”
Very stable
  Water pipes are resistant to corrosion
  Paint is durable and resistant to moisture and mold
  In gasoline, it raises temperature and pressure at which pre-ignition or engine knocking occurs
Very dese
  Effective shield against radiation

## Slide 8: Common forms of lead
Lead acetate
  White, crystalline substance
  Sugar of lead has a sweet taste
  Paint
Lead tetraethyl
  antiknock compound added to gasoline
  significant contributor to air pollution

## Slide 9: What are the Health Effects associated with lead exposure?
Encephalopathy
Colic
Anemia
Hemoglobin Synthesis
Peripheral Neuropathies
Infertility
Systolic Blood Pressure
Nerve Conduction Velocity
Erythrocyte Protoporphyrin
DEVELOPMENTAL TOXICITY
IQ, Memory, Learning
Growth
Notes: We will go into more detail of these health effects in the next lecture.

## Slide 10: Where can we find in the environment?
Varies from place to place
Soil near roadways (pre-1976 gasoline)
Soil near homes (paint)
Elevated in soil, water, or air near lead mining or smelting facilities
Near smaller businesses and industries that involve lead

## Slide 11: How did Lead get into the Environment?
Deterioration of lead-based paint
  Banned 1978
  Still used in industrial paint
Leaded gasoline
  Started 1923
  Phase out started in 1976
  Still allowed in airplane gas
Lead service lines in water distribution systems
  Banned in 1986
Industries that release lead, like mines, smelters

## Slide 14
Notes: Lead found in soil throughout New Orleans

## Slide 15: Sources of Lead in Drinking Water
Lead service lines (LSLs)
  Contributes ~ 50-75% of lead at tap
Leaded brass
  Prior to 2014, 8% lead allowed in “non-leaded” pipe
  Leaded-brass parts discharged enough lead to produce 0.5 - 2.4 IQ deficit in children consuming 2 L of water/day (Maas et al 2005)
Leaded solder
  Common in homes built before prohibited in 1986

## Slide 16: Even ”Lead-free” Plumbing has Lead
Safe Drinking Water Act Amendment (1986)
    Lead plumbing or solder in potable water systems prohibited
    “Lead-free” defined as:
      ≤0.2% lead for solders and flux
      ≤8% lead for pipe and pipe fittings
    Effective after June 1986
      LA did not implement until 1988
Reduction of Lead in Drinking Water Act (2011)
    “Lead-free” defined as:
      ≤0.2% in solder and flux
      ≤0.25% in plumbing
    Effective date of Jan 2014
      Louisiana set effective date for Jan 2013

## Slide 17: How to Check for a Lead Service Line
TOOLS NEEDED:
  Flathead Screwdriver or key
  Refrigerator magnet
Notes: http://gbwater.org/media/82002/lead-pipe-identification-brochure.pdf

## Slide 18: Locate the water service line coming into the building.
Pick a test area on the pipe in the middle of the entry point (where it comes into the building) and the inlet valve.
Use the edge of the screwdriver or they key to scratch through any corrosion that may have built up on the outside of the pipe.

## Slide 20: Lead Pipe
If the scraped area is shiny and silver, your lead service line is lead. A magnet will not stick to a lead pipe.

## Slide 21: Copper Pipe
If the scraped area is copper in color, your service line is copper! A magnet will not stick to a copper pipe.

## Slide 22: Galvanized Steel Pipe
If the scraped area remains a dull gray, and a magnet sticks to the surface, your service line is galvanized steel.

## Slide 23: Lead Paint Hazard Assessment
Notes: This is the Lead Paint demo
Give everyone a lead check stick and set out objects that may contain lead.
Follow instructions on Teacher notes

## Slide 24: Homework Assignment:
Check your water service line for a lead service line.
Using a lead check stick, test an object in your home that you suspect could contain lead.
Notes: They can take a picture of their findings and bring it to class, and/or write a short paragraph of their findings.